## Slide 1: NSF-NRT challenge A
Team insight : ppt and product made by Zelong Huang and Perry Liang

## Slide 2: Contents
1:Problem Statement & Mission
2:Hardware: High-Precision Sensing
3:Gateway & Data Processing Logic
4:Experimental Results & Visualization
5:Conclusion & Future Work

## Slide 3: Problem Statement & Mission
Problem: The Invisible Challenge
Safety Risks:Invisible alcohol vapors and hazardous leaks pose significant threats to public health and industrial safety.
Resolution Bottleneck: Standard 10-bit microcontrollers (4.88 mVper bit) are too coarse to capture subtle fluctuations.
Interference Vulnerability: Single-sensor nodes are highly susceptible to cross-sensitivity (e.g.smoke or cleaning agents), leading to frequent false alarms.
Mission:Redefinine Precision Sensing
Cross-Sensing Architecture:Integrating heterogeneous sensor array(MQ-2, 3, 9, 135) to achieve multi-dimensional environmental coverage.
Signature Fingerprinting: Utilizing data fusion to extract unique "chemical fingerprints," distinguishing target events from baseline drift.
High-Precision Insight: Leveraging 16-bit ADC resolution and PC-side algorithms to provide robust, laboratory-grade monitoring insights.

## Slide 4: Hardware: High-Precision Sensing
CoreArchitecture
Sensor Fusion: Integrated MQ-2, 3, 9, and 135 to capture a comprehensive "chemical fingerprint" instead of a single data point.
Precision Upgrade: Replaced Arduino’s internal 10-bit ADC with the ADS1115 (16-bit external ADC).
pic left below:simple MQ3-board
pic mid up:simple MQ3-board
pic mid below:simple MQ3-board
Key Advantages over Standard Setup
64x Resolution Boost:Improving detection granularity.
Programmable Gain :Capability to "zoom in" on micro-fluctuations in vapor concentration.
Noise Immunity:Utilizing ADS1115’s internal low-drift voltage reference to eliminate Arduino power rail interference.
Power Stability: Independent 5V external supply ensures reliable heater operation for the entire array

## Slide 5: Gateway & Data Processing Logic
Adaptive Feature Engineering
(Eliminating Environmental Drift and Signal Noise)
Dynamic Baseline Tracking:
Robust Scaling:
Adaptive Activation Trigger:
Multi-Sensor Fusion Scoring
（Heuristic Weighted Models for Gas Classification）
Alcohol Score (Targeted Sensitivity):
Smoke Score (Multi-Channel Sync):
Air Quality (Broad Spectrum):
System Health & Reliability
（Real-Time Data Quality Metrics）
Core Metric:
Stability (70%) + Signal Quality (30%)
Reliability Formula:
SNR Mapping (Signal-to-Noise Ratio):

## Slide 6: Experimental Results & Visualization

## Slide 7: Conclusion & Future Work
Conclusion: A Scalable Multi-Channel Framework
Success: Developed a functional, high-precision IoT hub capable of signature recognition for alcohol and smoke.
Reliability: Integrated real-time health monitoring (SNR & Packet Loss) to ensure data integrity.
Future Work：
Hardware：
Sensor Calibration: Address the lower-than-expected sensitivity of the MQ-3 sensor through advanced multi-point calibration.
Broadening Scope: Expand the testing database to include a wider variety of volatile gases.
Stress Testing: Evaluate system performance under extreme environmental conditions (high heat/humidity).
software：
Latency Reduction: Optimize the data polling cycle to minimize waveform delay between sensing and visualization.
Communication Stability: Resolve intermittent interface instability to lower the packet loss rate.
Robust Protocol: Implement error-correction algorithms to stabilize the serial-to-web data stream.

## Slide 8: THE END THANKS FOR WATCHING!